## Slide 1
StoragePrabhu99
Day 5
Dell EMC Storage Systems Hands-On Focus
Unity • VNX • PowerMax • Pools • LUNs • RAID • Unisphere • Snapshots • Replication • Provisioning
STUDENT CLASSROOM PRESENTATION
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems

## Slide 2
Learning outcomes
By the end of Day 5, you should be able to explain, navigate and simulate a storage provisioning workflow.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
2
Portfolio
Position Unity, VNX and PowerMax at overview level.
Architecture
Explain controllers, front-end connectivity, pools, LUNs and RAID.
Provisioning
Describe pool → LUN → access mapping → host validation.
Unisphere
Recognize common monitoring, provisioning and protection areas.
Protection
Explain snapshots and replication and distinguish them from backups.
Lab
Complete a simulated 500 GB LUN workflow and document evidence.

## Slide 3
Day 5 at a glance
The source curriculum uses an 8-hour flow that moves from portfolio → architecture → GUI → protection → lab.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
3
09:30–10:00
Recap + objectives
10:00–11:15
Dell EMC portfolio
11:30–13:00
Architecture + pools / LUNs / RAID
14:00–15:15
Unisphere walkthrough
15:30–16:30
Snapshots + replication
16:30–17:30
Provisioning lab
17:30–18:00
Quiz + review
Hands-on principle
Before clicking: state what object you are changing, why, who is affected, and what evidence should prove success.

## Slide 4
Connect Days 1–4 to Day 5
Vendor terminology changes; the storage administrator’s reasoning stays consistent.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
4
Day 1 DAS / NAS / SAN / RAID
Day 2 FC / iSCSI / zoning / LUN / MPIO
Day 3 virtualization / tiering / performance
Day 4 backup / DR / replication / RPO / RTO
Day 5 Dell EMC implementation + lab

## Slide 5
Dell Technologies storage portfolio — course scope
Unity, VNX and PowerMax are intentionally taught at different depth levels.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
5
UNITY
Focus: enterprise platform, architecture, provisioning and Unisphere concepts.
VNX
Use as an enterprise example for pools, LUNs, RAID and host access.
POWERMAX
High-end enterprise platform; focus on transferable storage concepts.
DELL TECHNOLOGIES • STORAGE
Training boundary: this module is overview + simulated administration, not a model-specific certification course.

## Slide 6
Portfolio comparison — what transfers?
Keep the comparison conceptual; validate model-specific capabilities in the actual lab.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
6
Dimension | Unity | VNX | PowerMax
Primary classroom use | Architecture + provisioning | Pools + LUNs + RAID + access | Architecture + provisioning model
Management focus | Unisphere | Unisphere | Unisphere for PowerMax
Common objects | Pools, LUNs, hosts | Pools, LUNs, storage groups | Storage groups, thin devices, masking views
Protection emphasis | Snapshots + replication | Snapshots / replication concepts | Local replication + SRDF concepts
Do not memorize product numbers. Learn the object model and the operational sequence.

## Slide 7
Unity — conceptual architecture
Map the generic enterprise path onto a Dell Unity platform.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
7
Host
SAN / Network
Front-end ports
Controllers
Pool
LUN
Student lens
• Where is capacity abstracted?
• Where does access get controlled?
• Where does the host discover the LUN?

## Slide 8
VNX — conceptual architecture
Use VNX to reinforce the classic storage objects and access workflow.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
8
Physical disks / RAID
Storage pool / RAID group
LUN
Storage group
Host
Modern teaching note
VNX is a legacy platform in today’s portfolio, but Dell still documents operational procedures for VNX/VNXe. Treat it as a transfer-of-concepts platform in this course.

## Slide 9
PowerMax — conceptual architecture
PowerMax adds a more explicit host/export object model.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
9
Host initiator group
Port group
Storage group
Thin devices
Masking view
Host access
PowerMax provisioning uses the association of initiators + front-end ports + storage group through a masking view.

## Slide 10
Common enterprise storage architecture
The source curriculum anchors Day 5 on this simple end-to-end mental model.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
10
Host
SAN / network
Front-end ports
Controllers
Storage pool
LUN / volume
capacity → protection → object → access → validation → monitoring

## Slide 11
Controllers, front end and back end
Keep internals conceptual unless the actual platform is available for demonstration.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
11
Front end
Receives host I/O over configured connectivity and exposes storage resources.
Controller layer
Coordinates access, cache and storage operations at platform level.
Back end
Coordinates access to underlying storage resources and protection layout.
Rule: use architecture-level language; do not invent vendor-specific implementation details.

## Slide 12
Storage pools
A pool abstracts physical storage resources into a capacity resource used for provisioning.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
12
POOL
LUNs / Volumes
• Capacity: enough usable headroom for workload growth
• Protection: aligned with workload and platform capabilities
• Performance: match workload profile and tiering goals
• Utilization: avoid over-commitment without monitoring

## Slide 13
Pool design: dynamic vs traditional
Exact support depends on Unity model and OE version.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
13
Concept | Dynamic pool | Traditional pool
Layout | Drive extents distributed across drives | More fixed storage/RAID-group style layout
Failure handling | Rebuild extents into distributed spare space | Rebuild behavior depends on configured RAID group
Operations | Designed for flexible pooled capacity | Common in legacy / specific configurations
Course action | Understand the pool as the provisioning abstraction | Understand the relationship between RAID groups and LUNs
Dell documents dynamic pools as the default for many Unity configurations; verify the actual platform before selecting pool type.

## Slide 14
RAID — protection before capacity
RAID choices trade capacity, resilience and rebuild behavior.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
14
RAID 1
Mirroring • strong redundancy • lower usable capacity
A
A
B
B
RAID 5
Single parity • efficient usable capacity • rebuild considerations
A
B
P
C
D
P
RAID 6
Dual parity • tolerates multiple drive failures
A
B
P
Q
C
D
P
Q
Always confirm supported RAID / protection choices in the actual lab or simulator.

## Slide 15
How should you choose protection?
Maximum usable capacity is only one decision criterion.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
15
Workload
Random I/O? Sequential? DB? Virtualization?
Resilience
How many drive failures must be tolerated?
Rebuild
What happens to performance during rebuild?
Growth
Can the pool be expanded / rebalanced?
Platform
What does this Dell platform actually support?

## Slide 16
LUNs — the logical block-storage object
A LUN becomes useful only when it is correctly presented to the intended host.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
16
Pool
Create LUN
Set access
Host discovers
OS / Hypervisor
LUN metadata usually includes name, ID, capacity and the pool / storage resource it consumes.

## Slide 17
Host access: mapping / masking
A visible LUN is not enough — the correct host must have the correct access.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
17
LUN
Access mapping
SAN zoning (if applicable)
Host
Validate identity
WWPN / iSCSI initiator / host object must match the intended server.
Validate scope
Avoid exposing the LUN to an unintended host.
Validate paths
Confirm redundancy / MPIO and expected discovery.

## Slide 18
End-to-end provisioning architecture
The lab follows the complete storage object lifecycle.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
18
Requirement
Pool
LUN
Access mapping
Host discovery
Validation
Plan → Select → Create → Present → Discover → Validate → Document

## Slide 19
Provisioning checklist
Run this checklist before clicking “Create”.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
19
☐ Capacity requirement understood
☐ Correct pool selected
☐ Protection requirement considered
☐ Correct LUN size + name
☐ Correct host / initiator identity
☐ Correct mapping / masking
☐ Host visibility confirmed
☐ Paths / MPIO validated
☐ Before / after evidence captured
☐ Documentation completed

## Slide 20
Provisioning — student decision exercise
Before the lab, verbalize the workflow for a 500 GB request.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
20
1 • Capacity
Where should 500 GB come from?
2 • Protection
What RAID / protection requirement applies?
3 • Access
Which host / initiators should see it?
4 • Validation
What evidence proves only the intended host sees it?
Instructor prompt
Do not start with the GUI. Start with the desired end state.

## Slide 21
SESSION 1 → SESSION 2
Unisphere & Daily Operations
Now translate the storage object model into a management interface and repeatable operational tasks.
21

## Slide 22
What is Unisphere?
Dell uses Unisphere-family interfaces for web-based array management; exact menus vary by product/version.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
22
Monitor
Health • capacity • performance • alerts
Provision
Pools • LUNs / volumes • host access
Protect
Snapshots • replication
Student principle: learn the object you are changing, not the button sequence.

## Slide 23
Unisphere navigation — Unity example
Official Dell documentation groups the interface into dashboard, system, storage, access, protection, events and support.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
23
Dashboard
System
Storage
Access
Protection & Mobility
Events
Support
System health
Look for component health, capacity, pool state and alerts.
Storage
Pools + block/file/VMware storage resources.
Access
Hosts + initiators + storage presentation.
Protection
Snapshot schedules + replication areas.
Events
Alerts + jobs + logs = evidence.

## Slide 24
Unisphere dashboard — simulated training visual
Not a production screenshot; use the actual lab interface for live navigation.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
24
Unisphere • Unity
DASHBOARD
SYSTEM
STORAGE
ACCESS
PROTECTION
EVENTS
SUPPORT
SYSTEM HEALTH
6.3 TB
Health
OK
Capacity
OK
Pools
OK
Performance
OK
SIMULATED UI • TRAINING VISUAL
What to notice
Health • capacity • pools • performance • alerts
Trainer action
Ask learners to name the object behind every dashboard tile.
Reference
Dell Unity Unisphere navigation includes Dashboard, Storage, Access, Protection & Mobility, Events and Support.

## Slide 25
Unisphere dashboard — what would you inspect first?
Use evidence before changing configuration.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
25
Health
Any component / resource not healthy?
Capacity
Free / used / preallocated / unconfigured?
Pools
Any pool approaching a threshold?
Performance
Latency / IOPS / throughput trend?
Alerts & Jobs
Did a prior task fail or raise a warning?

## Slide 26
Pool view — what should you verify?
A pool is a capacity + protection + performance decision.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
26
Unisphere • Storage → Pools
DASHBOARD
SYSTEM
STORAGE
ACCESS
PROTECTION
EVENTS
SUPPORT
SYSTEM HEALTH
6.3 TB
Health
OK
Capacity
OK
Pools
OK
Performance
OK
SIMULATED UI • TRAINING VISUAL
Capacity
Free / used / efficiency
Protection
Pool / tier / protection profile
Workload fit
Does this pool fit the application profile?

## Slide 27
Block / LUN view — simulated training visual
Look for the LUN object and its relationship to pool, size, ID and host access.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
27
Unisphere • Storage → Block
DASHBOARD
SYSTEM
STORAGE
ACCESS
PROTECTION
EVENTS
SUPPORT
SYSTEM HEALTH
6.3 TB
Health
OK
Capacity
OK
Pools
OK
Performance
OK
SIMULATED UI • TRAINING VISUAL
LUN Name
APP01_DATA01
Size
500 GB
Pool
POOL_APP
Host
APP01_ESX

## Slide 28
Access / host view — simulated training visual
Access configuration is where a correct LUN can still become a wrong service.
RPS | ICICI • Day 5 • Dell EMC Storage Systems
28
Unisphere • Access → Hosts / Initiators
DASHBOARD
SYSTEM
STORAGE
ACCESS
PROTECTION
EVENTS
SUPPORT
SYSTEM HEALTH
6.3 TB
Health
OK
Capacity
OK
Pools
OK
Performance
OK
SIMULATED UI • TRAINING VISUAL
Check identity
WWPN / iSCSI initiator / host object
Check mapping
Which LUNs / volumes are assigned?
Check paths
Expected redundant paths / MPIO?

## Slide 29
Jobs, alerts and logs — operational evidence
A GUI action should leave a trace that can be validated.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
29
Jobs
Did the create / modify task complete?
Alerts
Did the system generate warnings?
Logs
What timestamps / events support the story?
Before / after
Can you prove the change had the intended effect?
Evidence-first sequence
Observe
Change
Job
Validate
Document

## Slide 30
Basic CLI / REST concepts
Use GUI for learning; CLI / API for repeatability and automation.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
30
Approach | Use in training | Strength
GUI / Unisphere | Visual provisioning and monitoring | Low barrier; easy to validate
CLI / UEMCLI | Repeatable administrative tasks | Scriptable / automatable
REST API | Integration and orchestration | Programmatic / tool-friendly
Example pattern — conceptual only
create pool → create LUN → assign host access → query job → validate
Dell EMC Unity Simulator download link: https://downloads.emc.com/usa/UnityVSA/DELLEMCUnityDemo-5.0.0.0-win.exe
Exact command syntax is version/platform dependent. Use the vendor guide for the lab environment.

## Slide 31
CLI provisioning mental model — Unity
The exact command string is version dependent; the object sequence is stable.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
31
Pool
LUN
Host / initiator
Access
Query / validate
Conceptual command shape
ACTION + OBJECT + TARGET + PARAMETERS
Operational rule
Never paste a command you do not understand into production.

## Slide 32
PowerMax provisioning objects
PowerMax uses explicit auto-provisioning objects for the host-to-storage relationship.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
32
Initiator group
Logical grouping of FC initiators.
Port group
Logical grouping of front-end ports.
Storage group
Logical grouping of thin devices.
Masking view
Association of initiator + port + storage groups.
Masking view = “who” + “through which ports” + “gets which devices”

## Slide 33
PowerMax Unisphere — simulated workflow
Dell documents a Host wizard plus a storage provisioning wizard; Solutions Enabler and REST APIs are also available.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
33
Create host
Select initiators
Create / select storage group
Create / select port group
Create masking view
Training visual
Use the actual PowerMax Unisphere interface in the lab/video. This slide shows the object sequence, not a product screenshot.
Pls refer for Demolab: https://democenter.dell.com/hol/HOLA/HOL-0504-01

## Slide 34
VNX Unisphere provisioning workflow
Use VNX to reinforce classic pool / LUN / storage-group access concepts.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
34
Storage pool
Create LUN
Add LUN to storage group
Set host LUN ID
Host discovers
Legacy terminology
VNX procedures may mention storage groups, HLU and MetaLUN. Treat these as platform-specific terms that map back to the common provisioning model.

## Slide 35
PROTECTION & MOBILITY
Snapshots & Replication
Protection choices become meaningful only when you ask what failure you are trying to recover from.
35

## Slide 36
Snapshots — point-in-time protection
A snapshot records a point-in-time state / changed data for a storage resource.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
36
10:00
SNAP
10:15
SNAP
10:30
SNAP
10:45
SNAP
Useful for
Fast rollback / recovery from accidental changes, corruption or deletion when the snapshot is accessible.
Boundary
A snapshot is not automatically an independent backup; it can depend on the underlying storage system.

## Slide 37
Unity snapshots — what Dell documents
Use actual platform/version behavior in the lab.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
37
Create / manage
Snapshots can be created for storage resources such as LUNs; schedules can automate protection.
Storage dependency
Dell notes that LUN snapshots are not intended as mirrors, DR or HA tools and may become inaccessible if the primary LUN is inaccessible.
Protection capacity
Snapshot capacity consumes protection space; monitor capacity and retention.
Operational question: “What happens to this recovery mechanism if the primary array is unavailable?”

## Slide 38
Replication — remote recovery copy
Replication moves or maintains data/changes at another storage location.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
38
Primary array
Replication link
Remote array
DR / Recovery
Use case
Site failure, array failure, maintenance or planned mobility.
Planning
Network, distance, bandwidth, change rate and RPO / RTO matter.
Validation
A replication session that exists is not the same as a tested recovery procedure.

## Slide 39
Unity replication — current concepts
Dell documentation supports synchronous and asynchronous replication for relevant storage resources.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
39
Mode | Core idea | Typical teaching lens
Synchronous | Writes are coordinated with a remote copy before the operation is considered complete | Low / zero RPO design where distance and latency allow
Asynchronous | Local write proceeds and remote synchronization follows | Non-zero RPO with distance / bandwidth flexibility
Unity example
Dell documents native replication for LUNs, LUN groups, VMFS / NFS datastores and other resources; exact supported combinations depend on release / configuration.

## Slide 40
PowerMax replication — SRDF at a glance
PowerMax environments commonly use SRDF-family replication for remote protection and mobility.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
40
R1 / source
SRDF link
R2 / target
Recovery / DR
Unisphere
Dell documents Unisphere for PowerMax functions for storage, data protection, SRDF views and monitoring.
SRDF / Metro
A synchronous active-active style use case exists within the PowerMax / VMAX ecosystem, with specific prerequisites.
Course boundary
Learn the replication object and recovery flow; do not memorize every SRDF state code today.

## Slide 41
Snapshot vs replication vs backup
Three mechanisms — three different protection roles.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
41
Mechanism | Where is the copy? | Typical recovery use | Key boundary
Snapshot | Often same storage system | Fast point-in-time rollback | May share failure domain with primary
Replication | Remote / secondary storage | Site / array recovery | Can replicate corruption / deletion
Backup | Separate backup workflow / media | Restore and long-term recovery | Restore must be designed and tested
Use the right mechanism for the failure mode.

## Slide 42
Protection scenario exercise
Decide what protection mechanism(s) address each failure.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
42
Accidental deletion
Snapshot + backup
Storage-system failure
Replication + backup
Site loss
Remote replication + backup + DR process
Discuss: what is the recovery point, where is the copy, and what is the dependency?

## Slide 43
HANDS-ON
500 GB LUN Provisioning Lab
Use the simulated lab / video to practice the full lifecycle: plan → pool → LUN → access → validation → documentation.
43

## Slide 44
Lab scenario — application requests 500 GB
You are the storage administrator. Your job is to provision safely, not just quickly.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
44
Request
500 GB block-storage resource
Target
Named application host / initiator supplied by instructor
Success
Correct host sees the LUN; unintended hosts do not

## Slide 45
Lab pre-check — gather the inputs
Do this before opening the provisioning wizard.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
45
Capacity
500 GB usable requirement
Pool
Target pool and available capacity
Protection
Required RAID / protection profile
Host
Host name + initiator identity
Protocol
FC or iSCSI
Validation
What should the host discover?

## Slide 46
Lab step 1 — select the pool
Choose the pool using workload + capacity + protection reasoning.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
46
POOL_APP
Free capacity
Protection fit
Proceed
Evidence to capture
Pool name • free capacity • protection profile • timestamp
Do not do
Create the LUN first and “figure out the pool later.”

## Slide 47
Lab step 2 — create the 500 GB LUN
Name it clearly and verify the selected pool before submission.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
47
POOL_APP
APP01_DATA01
500 GB
Create job
Completed
Capture: LUN name • size • pool • job status

## Slide 48
Lab step 3 — configure host access
Select the intended host identity and the appropriate protocol / access path.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
48
Identity
APP01-ESX WWPN / iSCSI initiator from instructor
Mapping
Assign the LUN to the host or host group
Safety check
Confirm no unintended host is selected
Think “least required access” — present only what the workload needs.

## Slide 49
Lab step 4 — validate host visibility
A successful array job is only half the job.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
49
Array job PASS
Host mapping CORRECT
Fabric / network UP
OS discovery VISIBLE
MPIO EXPECTED PATHS
Validation evidence
Screenshot / job record / host rescan / path count / LUN ID

## Slide 50
Lab step 5 — document the provisioning result
Operations is not complete until the configuration is recorded.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
50
Field | Value
LUN name | APP01_DATA01
Size | 500 GB
Pool | POOL_APP
Host | APP01-ESX
Host / initiator identity | ________________
Access / mapping | ________________
Validation result | PASS / FAIL

## Slide 51
Simulated Unisphere task board
Use this slide as the lab runbook while the real interface or video is on screen.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
51
① Dashboard
Confirm health
② Storage → Pools
Select target pool
③ Storage → Block
Create 500 GB LUN
④ Access → Hosts
Map to intended host
⑤ Events → Jobs
Capture completion evidence
⑥ Host / OS
Rescan + validate

## Slide 52
Troubleshooting — LUN not visible
Walk the chain from storage object to host OS; collect evidence before changing configuration.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
52
Object exists
Host mapping
Fabric / network
Host discovery
Multipath
Golden rule: symptom → evidence → hypothesis → corrective action → validation

## Slide 53
Troubleshooting — high latency
Do not jump directly to RAID changes. Establish scope first.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
53
Host
Path / fabric
Controller / front end
Pool
Media / devices
Ask
Is the latency broad or isolated to one workload?
Check
Capacity pressure • queueing • alerts • path health
Validate
Correlate before / after any change.

## Slide 54
Troubleshooting — snapshot / replication issues
Treat protection features as stateful workflows with dependencies.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
54
Snapshot issue
Check state • capacity • retention • intended recovery action
Replication issue
Check source • target • link • session state • lag / errors
Recovery issue
Verify that the protected copy is actually usable, not merely “configured”.

## Slide 55
Team design challenge — 2 TB workload
Design the storage workflow; document assumptions that must be validated on the actual Dell platform.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
55
2 TB workload
Pool
Protection
LUN
Host access
Also specify
Snapshot / replication option • monitoring plan • validation evidence
Defend your decisions
Why this pool? Why this protection? How is the LUN presented? What will you monitor?

## Slide 56
Common operational mistakes
The fastest GUI path is not always the safest operational path.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
56
Create without requirement
Capacity and workload not understood
Map to wrong host
Identity / access not validated
Treat snapshot as backup
Same failure domain may remain
Change RAID immediately
No evidence / scope first
Skip before/after evidence
Hard to prove the result
Ignore documentation
Next engineer cannot reproduce the state

## Slide 57
Knowledge check — no notes
Answer in your own words before reviewing the next day.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
57
Q1
What is the purpose of a storage pool?
Q2
What is a LUN and how is it presented to a host?
Q3
Why must mapping / masking be validated?
Q4
What is Unisphere used for?
Q5
Why is a snapshot not automatically a backup?
Q6
What is the difference between replication and backup?
Q7
Name two evidence sources to check when a LUN is not visible.

## Slide 58
Recap — the Day 5 mental model
Keep these five ideas with you after the lab.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
58
01
Objects Pool → LUN → host access
02
Protection RAID + snapshot + replication are different layers
03
Management Unisphere is a view into storage objects and state
04
Validation Jobs + host discovery + paths prove the result
05
Operations Evidence + documentation make changes supportable

## Slide 59
One-page cheat sheet
Use this as the Day 5 quick reference during future storage operations.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems
59
ARCHITECTURE
Host → SAN → FE ports → controllers → pool → LUN
PROVISIONING
Plan → select pool → create LUN → map host → discover → validate → document
UNISPHERE
Monitor • Provision • Protect • Events / Jobs
PROTECTION
Snapshot = point-in-time • Replication = remote copy • Backup = managed recovery workflow
RULE
Collect evidence BEFORE changing configuration.

## Slide 60
Day 5 references
Course source material
• RPS_Storage_Keyskill_Day5(1).pptx — supplied Day 5 scope and learning objectives
• RPS_Storage_Keyskill_Day5_Instructor_Content.md — lab flow, architecture, troubleshooting and assessment
• Introduction to Storage & Backup_ITC.pptx — generic storage, SAN, LUN, RAID, backup and replication concepts
Current Dell references used for vendor-specific detail
• Dell Unity: Unisphere Overview — GUI navigation, dashboard, pools, block, hosts, protection, alerts and jobs
• Dell Unity Family: pool, LUN, snapshot and replication guides
• Dell PowerMaxOS / Unisphere for PowerMax — storage groups, initiators, port groups, masking views and SRDF
• Dell VNX knowledge-base procedures — storage pools, LUNs, storage groups and HLU / MetaLUN examples
TRAINING NOTE
Use the actual lab model/version for live screenshots and exact menu / CLI syntax.
storageprabhu99@gmail.com• Day 5 • Dell EMC Storage Systems