## Slide 1
StoragePrabhu99|DAY 9
Troubleshooting & Real-World Scenarios
Disk failures • Controller errors • Logs • Alerts • SNMP traps • Multipath • RCA • Banking case studies • Scenario drill
StoragPrabh99| Storage Keyskill Training
09

## Slide 2
Learning Objectives
Turn storage knowledge into evidence-based operational judgment.
2
💿
Disk failures
Investigate affected drive, enclosure, redundancy and rebuild state.
🧠
Controller errors
Correlate controller state, failover, path and workload impact.
📜
Logs & alerts
Build timelines and distinguish signals from root cause.
♻️
Multipath
Separate host, fabric, path and storage failure domains.
📝
RCA
Write symptom, impact, cause, correction and prevention.
🏦
Banking scenarios
Apply the method to business-critical training cases.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios

## Slide 3
Day 9 in the Learning Journey
Use Days 1–8 knowledge as evidence, not isolated theory.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
3
Storage basics
SAN / provisioning
Performance / virtualization
Backup / DR
Dell EMC
NetApp
HPE / IBM
Monitoring / security
DAY 9: Integrate
The objective is not to know every error code. It is to reduce the fault domain with evidence.

## Slide 4
8-Hour Delivery Plan
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
4
Time
Topic
Primary learning mode
09:30–10:00
Recap + troubleshooting method
Framework + discussion
10:00–11:15
Disk failures + controller errors
Case walkthrough
11:15–11:30
Break
—
11:30–12:45
Logs + alerts + SNMP traps
Timeline analysis
12:45–13:30
Multipath failover
Path isolation
13:30–14:30
Lunch
—
14:30–15:30
RCA writing
Template + example
15:30–15:45
Break
—
15:45–16:45
Banking case studies
Team analysis
16:45–17:45
Team scenario drill
Time-boxed incident
17:45–18:00
Debrief + Day 10 bridge
Reflection

## Slide 5
Master Troubleshooting Model
Never jump from symptom to fix.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
5
1
Define symptom
2
Collect evidence
3
Scope fault
4
Form hypothesis
5
Test
6
Fix
7
Validate
8
Document
Goal: reduce the fault domain before taking a corrective action.

## Slide 6
Incident First Look: What Is the Symptom?
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
6
A
User report
“Application response time increased.”
M
Monitoring signal
“Storage warning generated.”
!
Operator temptation
“Replace a disk now.”
Correct first move
Define scope + collect evidence + establish timeline

## Slide 7
Evidence Hierarchy
Correlate evidence across layers before deciding the cause.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
7
✓
Storage
drive state • controller state • pool health
✓
Fabric / Network
link state • errors • path events
✓
Host
MPIO • rescan • OS events
✓
Virtualization
datastore • VM path • hypervisor alerts
✓
Application
latency • timeout • service impact
One layer alone rarely proves root cause.

## Slide 8
Session 1
Disk failures, controller errors, logs, alerts, SNMP traps and multipath.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
8

## Slide 9
Disk Failure — What to Check
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
9
Identify affected disk/drive, enclosure and storage system.
Check whether redundancy is intact and whether rebuild/degraded state is present.
Review correlated alerts/logs for additional failures.
Assess workload impact plus capacity/protection exposure.
Follow the approved replacement/rebuild procedure for the actual platform.
Drive failure
↓
Degraded protection?
↓
Rebuild / fault domain
↓
Workload impact
↓
Approved recovery

## Slide 10
Disk Failure — Evidence Collection Checklist
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
10
Checkpoint
Evidence
Why it matters
Object
Drive ID / enclosure / state
Confirms exact component
Protection
RAID / pool / redundancy state
Shows exposure during rebuild
Timeline
First disk alert timestamp
Separates cause from consequences
Performance
Latency / IOPS / queueing
Shows workload impact
Recovery
Rebuild / replacement status
Confirms restored protection
Evidence before action

## Slide 11
Controller Errors — Start with the Timestamp
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
11
1
1 • Controller event
Capture exact time, object and severity.
2
2 • Peer / failover state
Check controller health and failover behavior.
3
3 • Correlated impact
Inspect paths, host multipath and application symptoms.
Platform-specific recovery steps come only after the actual environment is identified.

## Slide 12
Controller Error — Fault Domain Map
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
12
Host
MPIO / OS
Fabric
links / zoning
Storage
controller / cache
Workload
latency / timeouts
Ask: where did the first verified abnormal state appear?

## Slide 13
Logs — Build the Incident Timeline
RPS | ICICI • Day 9 • Troubleshooting & Real-World Scenarios
13
10:02:11
Host latency rises
10:02:18
Storage warning
10:02:21
Controller event
10:02:23
Path change
10:03:04
Application timeout
The first abnormal event is not always the most visible alert.

## Slide 14
Alerts — Signal, Not Automatically Root Cause
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
14
Signal type
What it tells you
What it does not prove
Hardware alert
Object changed state
That object is root cause of service impact
Capacity alert
Threshold was crossed
That capacity caused the incident
Path alert
Connectivity changed
That storage is unhealthy
Performance alert
Metric moved beyond threshold
Why the metric moved
Treat alerts as evidence to correlate with state, timeline and impact.

## Slide 15
SNMP Traps — Asynchronous Notifications
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
15
Storage device
SNMP agent
Monitoring server
Trap receiver
Operator
Triage
Trap = notification. The investigation still needs timestamps, affected object, current state and correlated evidence.

## Slide 16
SNMP Trap Analysis Worksheet
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
16
Field
Capture
Source device
________________________
Trap / event type
________________________
Timestamp
________________________
Affected object
________________________
Related storage alert
________________________
Host / application impact
________________________

## Slide 17
Logs + Alerts + Traps — Correlation View
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
17
E
Logs
Detailed chronology
E
Alerts
Action-oriented signal
E
SNMP traps
Asynchronous notification
Join on common keys
timestamp • device • object • severity • impact

## Slide 18
Multipath — Intended Redundant Design
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
18
HOST
STORAGE
Path 1
Path 2
Path 3
Redundancy should survive a single path failure without losing the LUN.

## Slide 19
Multipath Failover — What to Verify
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
19
Did the alternate path remain healthy?
Did the host multipath stack transition as expected?
Was redundancy reduced but service preserved?
Where did the failed path break: host, fabric/network or storage?
After repair, is the intended path count and health restored?
Path state
Path
State
1
UP
2
FAILED
3
UP

## Slide 20
Multipath Failure Scenario
A single path fails; the application remains online.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
20
✓
Observed
Application continues. One path shows DOWN.
E
Evidence to collect
Host MPIO + switch port + storage target port.
→
Decision
Repair failed path; preserve redundancy.
Do not declare “fixed” until path redundancy is restored and validated.

## Slide 21
Multipath Scenario — Isolate the Fault Domain
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
21
?
Host
MPIO state • HBA/NIC
?
Fabric
link • errors • zoning
?
Storage
target port • controller
Evidence-supported statement: “Failure is isolated to ______ because ______.”

## Slide 22
Session 1 Knowledge Check
Pause and answer before moving to RCA.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
22

## Slide 23
Quick Check — Disk + Controller
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
23
Question
Key idea
What do you inspect first after a disk alert?
Object identity, redundancy/protection state and timeline
Why inspect controller peer/failover state?
To understand continuity and correlated path effects
Why not replace hardware immediately?
The alert may be secondary or unrelated to impact
What validates recovery?
Service health + restored redundancy

## Slide 24
Quick Check — Multipath
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
24
Q
Question
What happens when one path fails?
A
Answer direction
Alternate path should carry I/O if design and configuration allow it.
✓
Validation
Confirm host MPIO state and recovered path health.

## Slide 25
Evidence-First Habit
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
25
SYMPTOM
→
EVIDENCE
→
FAULT DOMAIN
→
HYPOTHESIS
→
TEST
→
VALIDATE
“I have a warning” is not a root-cause statement.

## Slide 26
Session 2
RCA writing, banking case studies and team-based scenario drill.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
26

## Slide 27
RCA — What a Good Analysis Separates
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
27
R
Incident summary
What happened and when?
R
Impact
What workload/service was affected?
R
Evidence
What facts support the finding?
R
Root cause
What condition initiated the incident?
R
Corrective action
What restored service?
R
Prevention
What reduces recurrence?

## Slide 28
RCA Structure — From Symptom to Prevention
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
28
Section
Example content
Symptom
Application timeouts began at 10:02
Impact
Database workload lost normal performance
Timeline
Storage → controller → path events
Root cause
Verified initiating fault based on evidence
Correction
Restored failed component/path
Validation
Service recovered + redundancy restored
Prevention
Monitoring, design or process improvement

## Slide 29
RCA Anti-Patterns
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
29
!
“Disk failed, RCA complete.”
Too little evidence.
!
“The alert caused the outage.”
Alert ≠ causation.
!
“We replaced it and it worked.”
No validation / prevention.
!
“Network issue.”
Fault domain too broad.
Better: state the observed fact, evidence, verified cause, action and validation.

## Slide 30
RCA Writing Template
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
30
Incident summary
Impact
Timeline / evidence
Root cause
Corrective action
Validation
Prevention

## Slide 31
Banking Case Studies — Important Framing
These are simulated training scenarios, not claims about actual bank incidents.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
31
🏦 Banking operations amplify the need for evidence-first storage troubleshooting because payment, ATM, core-banking and online services can be tightly coupled to infrastructure dependencies.
B
Case A
Payment database latency
B
Case B
ATM storage path degradation
B
Case C
Online banking DR storage event

## Slide 32
Case A — Payment Database Latency
Training scenario
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
32
S
Symptom
Payment transactions slow down.
E
Known evidence
Storage latency warning at same time.
?
Question
Is storage the cause, consequence or coincident signal?
Student task
Build a 5-event timeline
Identify missing evidence
State one test before making a change

## Slide 33
Case A — Evidence Pack
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
33
Evidence
Value
Host latency graph
Confirms application-side symptom
Array performance
Shows storage-side behavior
Controller event log
Tests controller hypothesis
SAN path events
Tests path/fabric hypothesis
Application timestamps
Correlates business impact
Expected output: evidence-supported fault domain + next test.

## Slide 34
Case B — ATM Storage Path Degradation
Training scenario
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
34
ATMs remain online, but one storage path reports repeated errors.
B
Host
MPIO shows one degraded path
B
Fabric
One switch-port error counter rises
B
Storage
Target port remains healthy
Question: where is the fault domain narrowing?

## Slide 35
Case B — Recovery & Validation
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
35
Stage
Expected evidence
Containment
Service still online / redundancy reduced
Repair
Failed path component restored
Recovery
MPIO path returns to healthy
Validation
Traffic balanced / expected path count
Prevention
Trend and alert reviewed

## Slide 36
Case C — Online Banking DR Storage Event
Training scenario
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
36
!
Trigger
Replication lag rises during a storage event.
R
Business concern
Recovery point may widen.
E
Investigation
Check storage, link, target and workload evidence.
Connect Day 4: recovery planning starts with RPO/RTO and must be validated end-to-end.

## Slide 37
Case C — Investigation Checklist
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
37
Replication state and lag
Source and target health
Connectivity / link health
Recent workload change rate
Snapshot / protection state
Business recovery requirement (RPO/RTO)
Validation evidence after stabilization
RCA question
What changed first?
What proves it?
What prevents recurrence?

## Slide 38
Cross-Case Comparison
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
38
Scenario
Primary risk
Key evidence
Payment latency
Performance / availability
Host + array + timeline
ATM path degradation
Redundancy consumption
MPIO + fabric + target port
Online banking DR
Recovery point exposure
Replication + link + RPO/RTO
Same method, different business context.

## Slide 39
Team-Based Scenario Drill
25 min investigation + 7 min presentation
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
39
R
Incident Lead
Owns timeline + decisions
R
Storage Engineer
Array evidence
R
Network / Fabric
Path evidence
R
Host Engineer
MPIO / OS evidence
R
RCA Recorder
Documents conclusion
Use only evidence in the scenario. State assumptions explicitly.

## Slide 40
Scenario Drill — Student Output
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
40
Symptom
Timeline
Evidence
Fault domain
Root-cause hypothesis
Corrective action
Validation
Prevention
7-minute team presentation

## Slide 41
Scenario Drill — Evidence Pack Example
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
41
Time
Source
Event
09:41:02
Host
Latency spike
09:41:05
SNMP trap
Target path warning
09:41:06
Switch
CRC error counter rises
09:41:08
Storage
Controller health normal
09:41:12
App
Transaction timeouts
Question: which signal is earliest, and which one is merely most visible?

## Slide 42
Scenario Drill — Decision Discipline
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
42
✓
Do
Preserve service and collect evidence
✓
Do
Use reversible tests where possible
!
Avoid
Changing multiple layers at once
!
Avoid
Declaring RCA from a single alert

## Slide 43
Team Debrief — What Would You Change?
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
43
After the incident is closed, ask:
Was the first alert the root cause?
What evidence was missing?
Which control detected the issue fastest?
Could the topology have reduced the impact?
What monitoring / runbook / training change should follow?

## Slide 44
Troubleshooting Across Vendors
The platform changes; the reasoning model stays consistent.
RPS | ICICI • Day 9 • Troubleshooting & Real-World Scenarios
44
Layer
Dell EMC
NetApp
HPE / IBM
Storage object
LUN / pool
Volume / LUN
Volume / pool
Access
Mapping / masking
SVM / LUN / export
Host / volume mapping
Protection
Snapshot / replication
Snapshot / SnapMirror
Snapshots / replication
Evidence
GUI / logs
System Manager / CLI
GUI / logs
Troubleshooting checkpoints remain: object → access → path → host → workload.

## Slide 45
Operational Runbook — Incident Start
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
45
Minute
Action
0–2
State impact + affected services
2–5
Freeze assumptions; collect primary alerts/logs
5–10
Normalize time + identify first abnormal event
10–15
Scope fault domain
15–20
Test hypothesis
20+
Correct, validate, document

## Slide 46
Operational Runbook — Safe Change Principles
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
46
Preserve evidence before altering configuration.
Prefer the smallest reversible action that tests the hypothesis.
Avoid simultaneous changes across storage, fabric and host.
Confirm business impact before disruptive recovery actions.
After action: validate service + redundancy + monitoring state.

## Slide 47
Troubleshooting — LUN Not Visible
RPS | ICICI • Day 9 • Troubleshooting & Real-World Scenarios
47
Object exists / healthy
Host access / mapping
Fabric / network
Host discovery
Multipath
OS / application
Same evidence-first sequence used in Days 5–8.

## Slide 48
Troubleshooting — High Latency
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
48
L
Host
latency / queue
L
Fabric
errors / drops
L
Controller
front-end state
L
Pool / media
capacity / contention
Do not jump directly to RAID changes. Establish evidence and scope first.

## Slide 49
Troubleshooting — Alert Storm
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
49
20 alerts arrive within 60 seconds.
Alert 1
Alert 2
Alert 3
Alert 4
Alert 5
Collapse duplicates → identify earliest event → correlate → prioritize action

## Slide 50
Troubleshooting — Snapshot / Replication Problem
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
50
Problem signal
Evidence to inspect
Snapshot unavailable
snapshot state • capacity • retention • recovery target
Replication lag
source • target • link • lag trend • change rate
Target unavailable
target health • network • relationship state
Unexpected failover
timeline • path state • recovery procedure

## Slide 51
RCA Example — Concise, Evidence-Supported
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
51
Summary
At 10:02, payment workload latency increased and timeouts followed.
Impact
Service degradation for the affected workload.
Cause
State only after evidence verifies the initiating fault.
Correction
Action taken to restore service.
Validation
Service normal + redundancy restored + alerts cleared.
Prevention
Monitoring / design / runbook improvement.

## Slide 52
Knowledge Check — 10 Questions
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
52
1. What is the first action after a storage alert?
2. How do you find the first abnormal event?
3. Why correlate logs, alerts and SNMP traps?
4. What does multipath protect against?
5. What must be validated after path repair?
6. What belongs in an RCA?
7. Why are banking cases labelled training scenarios?
8. What evidence isolates fabric vs storage fault?
9. Why avoid multiple simultaneous changes?
10. What does good recovery validation prove?

## Slide 53
Knowledge Check — Answer Key
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
53
1. Define scope + collect evidence
2. Normalize timestamps; identify first abnormal event
3. To correlate signals and avoid single-source conclusions
4. Continued access when redundant path remains healthy
5. Healthy intended path count / MPIO state
6. Summary, impact, evidence, cause, correction, validation, prevention
7. They are simulated training scenarios
8. Cross-layer evidence + device/object state
9. To avoid obscuring the real cause
10. Service health + restored redundancy

## Slide 54
Student Cheat Sheet
Keep this beside you during incident drills.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
54
1
Define
Impact + scope
2
Collect
Logs + alerts + traps
3
Correlate
Time + object + source
4
Isolate
Host / fabric / storage
5
Hypothesize
Evidence-supported
6
Test
Small + reversible
7
Recover
Approved action
8
Validate
Service + redundancy
9
RCA
Cause + prevention

## Slide 55
Day 9 Takeaways
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
55
1
Evidence beats assumption.
2
The earliest abnormal event matters.
3
Multipath changes the fault domain, not the troubleshooting discipline.
4
RCA must connect evidence → cause → prevention.
5
Recovery is incomplete until service and redundancy are validated.

## Slide 56
Reference Map — Source Alignment
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
56
Source material
Used for
RPS Day 9 source deck
TOC, troubleshooting flow, cases, drill
RPS Day 9 instructor guide
Talk track, evidence method, RCA and drill timing
Days 1–8 RPS decks
SAN/MPIO, performance, DR, vendor platforms, monitoring
Storage-Module1 / ITC material
SAN, host paths, controllers, LUN and multipath concepts
Case-study note: banking incidents in this deck are intentionally simulated training scenarios.

## Slide 57
Reference — Core Source Statements
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
57
“Never jump from symptom to fix. The objective is to reduce the fault domain with evidence.”
“Treat logs, alerts and SNMP traps as evidence; none is automatically the root cause.”
“After recovery, validate both service health and restored redundancy.”

## Slide 58
Day 10 Bridge
From troubleshooting events to operational monitoring and continuous improvement.
RPS | ICICI • Day 9 • Troubleshooting & Real-World Scenarios
58
Incident evidence
Trend / monitoring
Capacity
Security
Governance
Operational maturity
Day 9 closes with incident reasoning. Day 10 turns that evidence into proactive operations.

## Slide 59
Final Challenge
One sentence from every learner: “My first action during a storage incident is…”
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
59
____________________________________________________________
____________________________________________________________
Use the method, not the guess.

## Slide 60
DAY 9 COMPLETE
Troubleshoot with evidence. Recover with discipline. Prove the fix.
storageprabhu99@gmail.com • Day 9 • Troubleshooting & Real-World Scenarios
60