## Slide 1
StoragePrabhu99
SAN, Fibre Channel,
and Storage Provisioning
DAY 2 • STUDENT PRESENTATION
From SAN building blocks and protocols to zoning, LUN presentation, thin provisioning and multipathing.
SAN BASICS
FC + iSCSI
ZONING
PROVISIONING
MPIO
HOST
HBA
FABRIC A
FC switch
FABRIC B
FC switch
STORAGE
Controller • LUN
8 HOURS
Architecture • Protocols • Provisioning • Resilience
Reference-led • vendor-aware • architecture focused

## Slide 2
Learning outcomes
By the end of Day 2, learners should be able to follow a block-I/O path from host to storage and explain how access is controlled.
1
Explain SAN
Hosts, HBAs, fabric, storage and the I/O path.
2
Compare protocols
SCSI, FCP/FC and iSCSI — what each layer does.
3
Explain zoning
WWNN/WWPN, soft vs hard, zones and zone sets.
4
Provision safely
LUN masking/mapping, thin/thick, MPIO and redundancy.
Learner lens
When a server needs storage, ask: who is the initiator, what is the target, which paths are permitted, and how is the LUN presented?
Source foundation: ITC Storage & Backup; Storage-Module1

## Slide 3
Day 2 roadmap
Two-session flow with architecture diagrams, protocol walkthroughs, provisioning logic and troubleshooting checkpoints.
01
SAN foundations
60 min
02
SCSI • FC • iSCSI
75 min
03
WWNs + zoning
75 min
04
Topologies + fabrics
60 min
05
LUNs + provisioning
90 min
06
MPIO + switch intro
70 min
07
Scenario lab + recap
50 min
Interactive moments
Draw a dual-fabric SAN
Name WWNN vs WWPN
Create a simple zone
Follow a LUN to the host
Fail one path and explain MPIO
Session plan for an 8-hour learning day

## Slide 4
01
SAN basics
A dedicated storage network that connects hosts to shared storage over block protocols.
APPLICATION
Database • VM • File service
HOST / OS
I/O stack • HBA
SAN FABRIC
FC switches • zoning
STORAGE ARRAY
Controllers • cache • RAID
LUN
Block device
SAN separates storage traffic from the general LAN and gives multiple hosts controlled access to shared block storage.
Source: ITC deck — SAN components and layered architecture

## Slide 5
SAN building blocks
Four logical layers are enough to understand most enterprise SAN diagrams.
01
Host
Servers, OS, HBA/CNA, multipath software
02
Fabric
FC switches/directors, ports, ISLs, zoning
03
Storage
Controllers, front-end ports, pools, RAID
04
Management
Switch/storage tools, monitoring, provisioning
Source: Storage-Module1; ITC SAN Components

## Slide 6
Host side: HBA, ports and multipath
The host converts application I/O into storage protocol traffic.
APPLICATION
SQL / VM / OS
OS STORAGE STACK
SCSI commands
HBA / NIC
FC or iSCSI
FABRIC
FC switch / IP
TARGET PORT
Storage front end
Host-side identifiers
WWNN — identifies the FC node/device.
WWPN — identifies a specific FC port.
iSCSI — uses initiator IQN instead of FC WWNs.
Design principle
Multiple independent host paths should reach redundant fabric components and storage target ports.
Source: ITC deck — HBA/CNA, WWN, multipath

## Slide 7
Storage side: target ports, controllers and LUNs
The array exposes logical block devices through front-end target ports.
HOST A
WWPN A1
HOST B
WWPN B1
FC FABRIC
Zones
ISLs
Name server
CTRL A
Target ports
CTRL B
Target ports
LUN 10
DB
LUN 20
VMFS / CSV
Target ports are network-facing storage interfaces; LUNs are logical block devices presented to hosts.
Source: ITC deck — storage controllers, ports and LUN presentation

## Slide 8
What is an I/O path?
A “path” is the end-to-end route between a host and a storage LUN.
HOST HBA 1
SWITCH A
TARGET A
LUN
PATH 1
If any component fails, the host may lose access unless another path exists.
HOST HBA 2
SWITCH B
TARGET B
PATH 2
MPIO combines or selects multiple physical paths as one logical disk access path.
Source: Microsoft MPIO guidance + ITC redundant SAN diagrams

## Slide 9
SAN traffic types
SANs can carry more than server-to-storage I/O.
Server → Storage
Normal application block I/O
Server → Server
High-volume inter-server traffic
Storage → Storage
Replication / backup without host intervention
The ITC reference explicitly describes server-to-storage, server-to-server and storage-to-storage interactions in a SAN.
Source: ITC Storage & Backup

## Slide 10
SAN vs LAN — keep the mental model clear
A SAN is not “just another LAN”. Its architecture is designed around storage I/O, isolation and resilience.
SAN
LAN
Primary workload
Block I/O
General IP traffic
Typical endpoints
HBA ↔ target port
NIC ↔ application endpoint
Protocols
FC/FCP, iSCSI
TCP/IP applications
Design focus
Low latency, redundancy, storage isolation
Broad connectivity, service diversity
Think
“Where does my data path run?” → Then identify the protocol, fabric and access-control layer.
Conceptual comparison; protocol details follow

## Slide 11
SCSI: the command language for block I/O
SCSI defines commands and semantics used by hosts to request block storage operations.
APPLICATION / FILE SYSTEM
SCSI COMMANDS
TRANSPORT
FC or TCP/IP
TARGET / LUN
Examples of SCSI commands: READ, WRITE, INQUIRY, TEST UNIT READY.
Important: SCSI is the storage command model; FC or iSCSI provide the transport path.
Source: ITC deck — SCSI and FC protocol explanation

## Slide 12
SCSI initiator and target
A simple way to visualize SCSI relationships before adding a SAN fabric.
INITIATOR
Host / HBA
SCSI COMMANDS
READ / WRITE / INQUIRY
TARGET
Storage port
LUN
Logical disk
In FC SANs, the host remains the initiator; the storage array exposes target ports and LUNs.
Source: ITC deck — SCSI client/server model

## Slide 13
Fibre Channel (FC) and FCP
Fibre Channel provides the storage network; FCP carries SCSI commands over FC.
SCSI
Commands
FCP
SCSI over FC
FIBRE CHANNEL
Frames / fabric
OPTICAL / SFP
Physical link
Useful mental model
SCSI = what the host asks for. FC/FCP = how the request travels to storage.
Source: ITC deck — FC/FCP

## Slide 14
iSCSI: SCSI over TCP/IP
iSCSI encapsulates SCSI commands and data and carries them across an IP network.
SCSI
Commands
iSCSI
Encapsulation
TCP
Reliable transport
IP / Ethernet
Network
TARGET
Storage
Why organizations choose iSCSI
Uses familiar Ethernet/IP skills and infrastructure.
Works well when IP networking is the preferred transport.
Still provides block-level storage access to applications.
Source: ITC deck — iSCSI fundamentals

## Slide 15
FC vs iSCSI — the decision is architectural
Both can provide block storage; the surrounding network, skills and resilience model differ.
Fibre Channel / FCP
iSCSI
Transport
FC fabric
TCP/IP Ethernet
Host interface
FC HBA / CNA
NIC / iSCSI initiator
Access control
FC zoning + array masking
IP/network controls + array masking
Typical design
Dedicated storage fabric
IP-based SAN
Operational emphasis
SAN fabric skills
IP networking + storage skills
Neither protocol eliminates the need for redundancy, access control and correct LUN presentation.
Source: ITC protocol sections; current Microsoft MPIO supports FC and iSCSI

## Slide 16
Protocol stack: FC vs iSCSI
Same logical storage request; different transport stack.
FC SAN
Application / FS
SCSI
FCP
Fibre Channel
Physical FC link
iSCSI SAN
Application / FS
SCSI
iSCSI
TCP/IP
Ethernet
Source: ITC protocol architecture

## Slide 17
FC port roles you should recognize
FC diagrams become easier once ports are named by role.
N_Port
Node-facing endpoint (host or storage)
F_Port
Switch port that connects an N_Port
E_Port
Expansion port used for an ISL between switches
NL_Port
Loop-attached node port used with FC-AL
Source: ITC deck — FC functional elements and SAN components

## Slide 18
FC addressing: WWN is the identity layer
World Wide Names are globally unique identifiers used to identify FC nodes and ports.
FC NODE
WWNN
World Wide Node Name
PORT 1
WWPN 1
PORT 2
WWPN 2
PORT 3
WWPN 3
One node can have multiple ports. Each port can have its own WWPN.
Source: ITC deck — WWN; terminology expanded for teaching

## Slide 19
WWNN vs WWPN
Remember the scope: node-level identity vs port-level identity.
Identifier
Scope
Teaching analogy
Where commonly used
WWNN
FC node / device
Building address
Node identity
WWPN
FC port
Apartment / interface
Zoning and port-level identification
Key point
For zoning, WWPN/pWWN-based identification is the practical port-level concept learners will see most often.
Source: ITC WWN content + Brocade zoning documentation

## Slide 20
Worked identity example
A dual-port HBA creates two independent WWPNs from one FC node.
HOST 01
WWNN: 10:00:...:01
HBA PORT A
WWPN: 50:00:...:A1
HBA PORT B
WWPN: 50:00:...:B1
FABRIC A
Switch A
FABRIC B
Switch B
ARRAY
Target ports
Zoning can be written around these port identities; MPIO can use the resulting independent paths.
Illustrative identifiers — not real WWNs

## Slide 21
Why zoning exists
Zoning limits which initiators and targets can discover and communicate with each other inside a fabric.
HOST 1
Initiator
HOST 2
Initiator
STORAGE A
Target
STORAGE B
Target
FC FABRIC
ZONE 1
Host 1 ↔ Storage A
ZONE 2
Host 2 ↔ Storage B
Without zoning, devices may have broader visibility than intended. Zoning creates the communication boundary.
Source: Storage-Module1 — zoning definition

## Slide 22
Zones, members and zone sets
The configuration hierarchy is: members → zones → zone set / configuration.
WWPNs / Ports
ZONE
ZONE
ZONE SET
ACTIVE
Example
Zone Z_DB01
Members: Host01-WWPN + ArrayA-Target1
Zone set: PROD_FABRIC_A
Contains all required production zones; one active configuration governs the fabric.
Source: Storage-Module1 — zones and zone sets

## Slide 23
Soft vs hard zoning — traditional terminology
Your reference deck uses WWN zoning = soft zoning and port zoning = hard zoning. Modern platforms may use hardware-enforced WWN/pWWN zoning as well.
Aspect
Soft zoning (WWN)
Hard zoning (port)
Definition
Membership based on WWN
Membership based on switch port
Identity
Moves with the WWN/device
Tied to the physical port
Operational effect
Flexible when device moves ports
Strong physical binding
Reference terminology
WWN zoning
Port zoning
Nuance
Do not equate “soft” with “unenforced”. Enforcement behavior depends on platform and zoning method; see current Brocade guidance.
Source: Storage-Module1 zoning types; Brocade current design guide

## Slide 24
Current practice: pWWN-based zoning
Brocade guidance recommends consistent identification methods and single-initiator zoning to reduce blast radius.
Recommended zone shape
1 INITIATOR
Host WWPN
1 TARGET
Array WWPN
Single-initiator / single-target zones minimize unrelated devices seeing each other.
Why it matters
Limits device visibility
Reduces change impact / RSCN scope
Simplifies troubleshooting
Supports cleaner provisioning patterns
External: Broadcom/Brocade SAN Design and Best Practices

## Slide 25
Zoning workflow
From discovery to an active zone configuration.
Discover WWPNs
1
Create aliases
2
Create zones
3
Build zone set
4
Activate config
5
Verify paths
6
Change control matters: validate identifiers, activate intentionally, then confirm host discovery and storage access.
Source: Storage-Module1 zoning workflow concepts; Brocade SANnav documentation

## Slide 26
Aliases make zoning readable
Use descriptive aliases so a zone can be understood without memorizing hexadecimal identifiers.
Alias
Identifier
Purpose
HOST01_P1
50:00:00:00:AA:01
Host HBA port
ARRAY01_T1
50:00:00:00:BB:01
Storage target port
ZONE_HOST01_DB
HOST01_P1 + ARRAY01_T1
Communication boundary
Naming pattern
<environment>_<host>_<port> | <array>_<role>_<port>
Illustrative naming convention

## Slide 27
Fabric topology
A fabric is built from one or more FC switches connected together; hosts and storage attach to the fabric.
HOST 1
HOST 2
SWITCH A
SWITCH B
STORAGE
Target ports
ISL
Fabric topology is the flexible, scalable FC topology highlighted in the reference deck.
Source: Storage-Module1 — Fabric Topology

## Slide 28
Point-to-point FC topology
Two devices are directly connected. Simple, but not expandable to three or more devices.
SERVER
N_Port
STORAGE
N_Port
Direct link
Use for learning
Good to explain the simplest FC relationship before introducing switches and fabrics.
Source: Storage-Module1 — Point to Point

## Slide 29
Fibre Channel Arbitrated Loop (FC-AL)
Devices share a logical loop; access is arbitrated rather than switched.
HOST
STORAGE
HOST
STORAGE
Shared loop • one direction • arbitration
Source: Storage-Module1 — Arbitrated Loop

## Slide 30
Why switched fabrics became the dominant enterprise pattern
Switching removes the shared-medium constraint of a loop and enables large, redundant fabrics.
Characteristic
FC-AL
Switched fabric
Connection model
Shared loop
Point-to-point via switches
Traffic
Arbitrated
Switched paths
Scalability
Limited
High
Enterprise redundancy
More constrained
Designed with dual fabrics / redundant paths
Source: Storage-Module1 — Fabric vs Arbitrated Loop

## Slide 31
Dual-fabric SAN design
The core resilience idea: do not make both paths depend on the same switch or fabric.
HOST HBA 1
HOST HBA 2
FABRIC A
Independent
FABRIC B
Independent
ARRAY CTRL A
ARRAY CTRL B
Failure domain separation
HBA / NIC
Cable
Switch
Storage front-end port
Source: ITC redundant SAN architecture + Microsoft MPIO resiliency concepts

## Slide 32
Inter-Switch Link (ISL)
An ISL connects FC switches so devices attached to different switches can communicate within the same fabric.
SWITCH A
E_Port
SWITCH B
E_Port
ISL
ISLs are part of the fabric’s connectivity and resilience design.
Source: Storage-Module1 — ISL

## Slide 33
SAN switches, directors and management
The physical platform changes, but the core role is still to route and manage storage traffic.
Switch
Typical edge / access connectivity.
Director
Higher port density and redundancy for large environments.
Management
Discover devices
Map servers and storage
Configure zoning
Monitor and alert
Source: Storage-Module1 — switch/director/management software

## Slide 34
Vendor examples — recognize the ecosystem
The concepts are vendor-neutral, but enterprise operations often use specific platforms.
Brocade / Broadcom
Cisco MDS
Dell PowerStore
NetApp ONTAP
HPE Storage
Examples from the reference material include Brocade and Cisco SAN switches, plus storage-array brands such as EMC/3PAR/NetApp/IBM.
Vendor examples are illustrative; configuration commands differ by platform

## Slide 35
Brocade-style zoning workflow (conceptual)
Vendor CLIs differ, but the object model is familiar: alias → zone → zone configuration → activate.
ALIAS DATABASE
ZONE DATABASE
ZONE CONFIG
ACTIVE FABRIC
HOST01_P1
50:00:...:A1
ZONE_DB01
Host01 + Array01
PROD_CFG
+ zones
FABRIC A
ACTIVE
Change management checkpoint → validate identifiers before activation.
Conceptual Brocade object model; command syntax intentionally omitted

## Slide 36
LUNs: the storage object a host actually consumes
A LUN is a logical unit of block storage presented by the storage system.
STORAGE POOL
Physical capacity
LUN
Logical block device
MASK / MAP
Access control
HOST
Disk device
FILESYSTEM
NTFS / VMFS etc.
Important
A LUN can exist on the array, but the host only uses it when access is correctly mapped/presented and the OS discovers it.
Source: Intelligent Storage System — provisioning/LUN concepts

## Slide 37
LUN masking
Masking controls which hosts can see a LUN in a shared environment.
HOST 01
Allowed
HOST 02
Not allowed
MASKING RULE
Host ↔ LUN permission
LUN 10
DB
LUN 20
Archive
Think: masking = “who is allowed to see this LUN?”
Source: Intelligent Storage System — LUN Masking

## Slide 38
LUN mapping / presentation
Mapping determines which host gets which LUN and, depending on platform, may also assign a host-visible identifier.
Host
Storage LUN
Host-visible ID
Purpose
APP01
LUN-101
Disk 10
Application data
DB01
LUN-201
Disk 20
Database data
VM01
LUN-301
Disk 30
VM datastore
Masking vs mapping
Masking = access boundary • Mapping/presentation = assignment of storage to a host.
Terminology varies by storage vendor; concept is consistent

## Slide 39
End-to-end LUN presentation flow
This is the sequence learners should be able to explain on a whiteboard.
1
Create pool / RAID
2
Create LUN
3
Identify host WWPNs
4
Zone host ↔ target
5
Mask / map LUN
6
Rescan + verify paths
A provisioning ticket is complete only when the host can see the intended LUN through the intended redundant paths.
Integrated workflow from the reference decks

## Slide 40
Thick (traditional) provisioning
Capacity is reserved up front and represented as allocated capacity to the host.
POOL
2 TB
LUN 1
500 GB
LUN 2
700 GB
LUN 3
800 GB
Capacity is committed to the logical volume according to the provisioning model.
Design question
How much capacity can I safely allocate today, and how much should remain unallocated for future workloads?
Source: Intelligent Storage System — traditional provisioning

## Slide 41
Thin provisioning
The host can see a larger logical capacity while the array consumes physical capacity as data is actually written.
HOST VIEW
THIN LUN
10 TB
Presented
→
PHYSICAL POOL
Allocated
3 TB
Free
7 TB
Actual data
2.2 TB
used
0.8 TB
free inside LUN
Thin provisioning separates logical presentation from immediate physical allocation.
Source: ITC — Thin Provisioning overview; Intelligent Storage System

## Slide 42
Thin vs thick — compare the operating model
The trade-off is not only capacity efficiency; it also changes monitoring and planning responsibilities.
Aspect
Thick
Thin
Logical capacity
Typically matched to allocated capacity
Can exceed immediately allocated physical capacity
Physical consumption
Reserved / committed earlier
Grows as writes consume pool capacity
Risk
Lower oversubscription risk
Requires capacity monitoring
Flexibility
Predictable
Higher elasticity
Operational focus
Allocation planning
Pool free space + overcommit governance
Operational rule
Never enable overcommit without monitoring the physical pool and alert thresholds.
Source: ITC thin provisioning + intelligent storage provisioning

## Slide 43
Thin provisioning: why arrays like it
The reference material highlights better capacity utilization and future-growth flexibility.
Avoid idle allocation
Only near-term physical capacity needs to be purchased.
Host sees future size
Applications can be provisioned for expected growth.
Centralized control
Pool capacity is managed from the array.
Watch oversubscription
Capacity planning and alerts become critical.
Source: ITC — Thin Provisioning benefits

## Slide 44
Multipathing (MPIO) basics
MPIO presents multiple physical I/O paths to the OS as one logical storage device.
HOST
OS
MPIO / DSM
Path selection
Failover
FABRIC A
FABRIC B
STORAGE
LUN
If one path fails, the host can continue I/O through another healthy path.
External: Microsoft Learn — MPIO troubleshooting and architecture

## Slide 45
MPIO architecture: what actually changes?
The application still sees one logical disk; MPIO manages the many underlying paths.
APPLICATION
OS DISK
MPIO
DSM / policy
PATHS
A / B / C / D
LUN
Typical path policies
Round-robin / balanced I/O
Failover-only / active-passive
Vendor-specific optimized paths
External: Microsoft Learn — MPIO / DSM concepts

## Slide 46
MPIO failure scenario
The simplest resilience test: remove one path and watch the application continue.
APP / DB
MPIO
PATH A
PATH B
STORAGE LUN
PATH A FAILS
MPIO detects the failed path and continues I/O on PATH B.
External: Microsoft Learn — MPIO fault tolerance

## Slide 47
MPIO design rules
Redundancy only works when the underlying paths are actually independent.
1
Different HBA / NIC
Separate host adapter failure domains.
2
Different switch
Avoid a single switch outage.
3
Different fabric
A/B fabrics isolate SAN failure domains.
4
Different target port
Use redundant storage front-end connectivity.
External: Microsoft Learn — redundant physical path guidance

## Slide 48
Switch configuration — what exists before zoning?
A SAN switch has physical ports, logical fabric identity, management access and fabric services.
Physical ports
SFP / transceiver / port state
Management
IP address, SSH/GUI, logs
Fabric identity
Domain ID / switch identity
Fabric services
Name server, zoning, RSCNs
Links
E_Ports / ISLs for fabric expansion
Vendor-specific commands differ; the architectural objects are stable.
Source: Storage-Module1 interconnecting devices and management

## Slide 49
Switch configuration: first-pass checklist
A safe introductory sequence for a new FC switch.
1
Rack / power / optics
2
Management IP + credentials
3
Set / verify fabric identity
4
Verify port speed and link state
5
Connect ISL only when fabric design is ready
6
Configure zoning
7
Validate host/storage discovery
Introductory workflow; exact commands vary by Brocade/Cisco platform

## Slide 50
Switch port state: the simple mental model
You can troubleshoot most early SAN issues by asking: is the port physically up, logged in, zoned, and presented?
PHYSICAL
Link up / optics / speed
LOGIN
FC device registered in fabric
ZONE
Initiator ↔ target allowed
PRESENT
LUN masked/mapped to host
OS
Host discovers the disk
This five-state model is useful for troubleshooting even when the vendor tools look very different.
Derived teaching framework from SAN provisioning and management concepts

## Slide 51
Troubleshooting: “Host cannot see the LUN”
Start at the path, not at the application.
1
Is the physical link up?
2
Did the host port log into the fabric?
3
Is the initiator in the correct zone?
4
Is the target port online and in the zone?
5
Is the LUN masked/mapped to the host?
6
Did the OS rescan / MPIO discover all paths?
Troubleshooting checklist aligned to provisioning workflow

## Slide 52
Scenario: new Windows database server
Work from the application requirement to the verified LUN.
App
DB01 requires 2 TB block storage
Host
Install / verify HBA + multipath
SAN
Zone DB01 WWPN ↔ array target
Array
Create LUN + mask/map to DB01
OS
Rescan; confirm multiple paths
Checkpoint
What could go wrong if the zone is correct but the LUN is not masked?
Classroom scenario

## Slide 53
Scenario: path failure in production
A well-designed SAN should survive a single path component failure without application interruption.
DB SERVER
MPIO
FABRIC A
FABRIC B
ARRAY
Failure injected: Fabric A switch goes offline.
Expected: I/O continues on Fabric B if the host and array paths are healthy.
External: Microsoft MPIO fault-tolerance guidance

## Slide 54
Knowledge check — protocol & topology
Discuss with a partner, then compare answers.
1. Is SCSI a transport or command model?
2. What is carried inside FCP?
3. What does iSCSI add to SCSI?
4. What is the key difference between fabric and FC-AL?
5. Why does a dual-fabric design need independent components?
Checkpoint • 5 minutes

## Slide 55
Knowledge check — zoning & WWNs
Can you map the right identity to the right access boundary?
Question
Answer to discuss
What does WWNN identify?
The FC node/device
What does WWPN identify?
A specific FC port
What does port zoning use?
Physical switch-port context
What does WWN/pWWN zoning use?
World Wide Name / port identity
Why use single-initiator zones?
Limit communication scope and change impact
Checkpoint • compare with your notes

## Slide 56
Knowledge check — provisioning & MPIO
Trace the dependency chain.
1
LUN exists
Array
2
Host is zoned
Fabric
3
LUN is masked/mapped
Array access control
4
Paths are visible
OS / MPIO
5
Application can use disk
Host
Question: which layer do you check first when the host sees no device at all?
Checkpoint • provisioning dependency chain

## Slide 57
Day 2 whiteboard exercise
Draw this from scratch without looking at the deck.
Design a dual-fabric SAN for one Windows database server and one storage array.
2 host paths
2 FC fabrics
2 array target paths
1 LUN
2 single-initiator zones per fabric
MPIO
Goal: explain the I/O path and the failure behavior when one fabric disappears.
Group exercise • 10 minutes

## Slide 58
Day 2 recap
The architecture now forms one connected mental model.
SAN
Dedicated block-storage network
SCSI
Storage command model
FC / FCP
Dedicated fabric transport
iSCSI
SCSI over TCP/IP
Zoning
Controls who can communicate
LUN masking/mapping
Controls host access to storage
Thin provisioning
Separates logical size from immediate physical allocation
MPIO
Uses multiple paths for resilience / policy
End-of-day recap

## Slide 59
Where this fits in the enterprise
SAN design supports availability, controlled access and operational scale — but only when the layers are configured together.
Business need
DB / VM / analytics
Architecture
SAN fabric + storage
Access
Zoning + masking
Resilience
Dual fabrics + MPIO
Operations
Monitoring + change control
Next: connect these foundations to storage arrays, administration and data protection.
Course progression

## Slide 60
References used for Day 2
Primary reference decks plus current vendor guidance used to modernize terminology and operational context.
Storage-Module1.pptx — SAN basics, zoning, VSAN, fabric, ISLs, topologies, switch/director, thin provisioning.
Introduction to Storage & Backup_ITC.pptx — SCSI, FCP/FC, iSCSI, SAN architecture, HBA/WWN, protocols, redundant SAN patterns.
2.Intelligent_Storage_System.pptx — storage provisioning, LUNs, masking, thin provisioning.
Microsoft Learn — MPIO troubleshooting / architecture and redundant path guidance.
Broadcom/Brocade — SAN Design and Best Practices; zoning and current pWWN / single-initiator guidance.
Vendor examples shown: Brocade/Broadcom, Cisco, Dell, NetApp, HPE; concepts remain vendor-neutral.
Student presentation • references and external validation